I/O Virtualization

---
I/O Virtualization
I/O Virtualization
Two ways of I/O virtualization
  - I/O virtualization in VMM
    - Rewritten Device drivers in VMM
    - + High performance
    - - High engineering cost
    - - Low fault tolerance (driver bugs)
  - Hosted I/O virtualization
    - Existing device drivers in a host OS
    - + Low engineering cost
    - + High fault tolerance
    - - Performance overheads
Guest VM
Guest VM
VMM
Block
device driver
Network
device driver
HW
Block device
Network device
Privileged VM
or Host OS
Guest VM
Guest VM
Block
device driver
Network
device driver
VMM
Most VMMs (except VMware ESX Server) adopt
hosted I/O virtualization
HW
Block device
Block device

---
I/O Virtualization
I/O Virtualization
I/O virtualization-friendly architecture
  - I/O operations are all privileged and trapped
    - Programmed I/O (PIO), memory-mapped I/O (MMIO), direct memory access (DMA)
  - Naturally full-virtualizable
    - “Trap-and-emulate”
    - Issues
      - 1. How to emulate various I/O devices
        - Providing a VM with well-known devices (e.g., RTL8139, AC97) as virtual devices
        - Existing I/O device emulators (e.g., QEMU) handle the emulation of well-known devices
      - 2. Performance overheads
        - Reducing trap-and-emulate cost with para-virtualization and HW support

---
Full-virtualization
Full-virtualization
Trap-and-emulate
  - Trap  hypervisor  I/O emulator (e.g., QEMU)
  - Every I/O operation generates trap and emulation
    - Poor performance
  - Example: KVM
I/O operation
QEMU
Guest VM
Host OS
(Linux)
MMIO or PIO
I/O emulation
Guest OS
vCPU
vCPU
User space
KVM (kernel module)
Kernel space
Native drivers
Trap
Interrupt

---
Para-virtualization
Para-virtualization
Split driver model
  - Front-end driver in a guest VM
    - Virtual driver to forward an I/O request to its back-end driver
  - Back-end driver in a host OS
    - Request a forwarded I/O to HW via native driver
I/O operation
QEMU
Guest VM
Host OS
(Linux)
Shared descriptor ring: Optimization by batching I/O requests
Reducing VMM
intervention cost
VirtIO
Backend
Guest OS
VirtIO
Frontend
User space
vCPU
vCPU
KVM (kernel module)
Kernel space
Native drivers

---
Para-virtualization
Para-virtualization
How to reduce I/O data copy cost
  - Sharing I/O data buffer (DMA target/source memory)
    - A native driver conducts DMA to guest VM’s memory
    - For disk I/O and network packet transmission
Xen grant table mechanism
Sec = 7
Dom = 1
REQ = R
GR = 1
DomainU(id=1)
Domain0(id=0)
Backend
driver
0
1
2
3
Native
Device driver
0	1	2	3	4
0	1	2	3	4
Response
Grant table
Physical frame number (PFN)
Disk
Machine frame number (PFN)
0	1	2	3	4	5	6	7	8	9
Xen
0
1
2
3
Active
Grant table
READ Sec 7
to PFN 3
Dom=0
MFN=6
Flag=R
Foreign Map
to PFN 2
for WRITE
with GR 1
Dom=0
MFN=6
Flag=R
DMA READ
request
Unmap

---
Para-virtualization
Para-virtualization
How about network packet reception?
  - Before DMA, VMM cannot know which VM is the destination of a received packet
    - Unavoidable overhead with SW methods
    - Two approches in Xen
Page flipping (remapping)
- Zero-copy
Page copying
- Single-copy
Network optimizations for PV guests [Xen Summit’06]
Domain0
DomainU
Domain0
DomainU
Buffer
Buffer
+ No copy cost
- Map/unmap cost
+ No map/unmap cost
   (some costs before optimization)
- Copy cost
Packet
Packet
Packet

---
Para-virtualization
Para-virtualization
Does copy cost outweigh map/unmap cost?
  - Map/unmap involves several hypervisor interventions
    - Copy cost is slightly higher than map/unmap (i.e., flip) cost
    - “Pre-mapped” optimization makes page copying better than page flipping
      - Pre-mapping socket buffer reduces map/unmap overheads
Page copying is the default in Xen
Network optimizations for PV guests [Xen Summit’06]

---
Why HW Support?
Why HW Support?
Why not directly assign one NIC per VM?
  - NIC is cheap HW
  - Technically possible
    - Selectively exposing PCI devices
    - Giving I/O privilege to guest VMs
    - Xen isolated driver domain (IDD)
  - But, unreliable and insecure I/O virtualization
    - Vulnerable to DMA attack
      - DMA is carried out with machine addresses
      - One VM can access another VM’s machine memory via DMA
      - How to prevent?
        - Monitoring every DMA request by using memory protection to DMA descriptor regions  Overhead!
Guest VM
Guest VM
Guest VM
VMM
Poor scalability: Slot limitation

---
HW Support: IOMMU
HW Support: IOMMU
I/O Memory Management Unit (IOMMU)
  - Presenting a virtual address space to an I/O device
    - IOMMU for direct I/O access of a VM: Per-VM address space
Virtual address
Virtual address
Physical memory
Level 2
Page
table
Level 2
Page
table
Page
table
MMU
IOMMU
Page
table
. / . / .
Page
table
Page
table
Page
table
Page
table
Level 1
Page
table
Level 1
Page
table
Intel VT-d
AMD IOMMU
ARM SMMU
Secure direct I/O device access

---
How to Deal with HW Scalability
How to Deal with HW Scalability
How to directly assign NICs to tens of hundreds of VMs consolidated in a physical machine?
  - PCI slots are limited
  - Can a single NIC support multiple VMs separately?
    - A specialized device for virtualized environments
      - Multi-queue NIC
      - CDNA
      - SR-IOV

---
HW Support: Multi-queue NIC
HW Support: Multi-queue NIC
Multi-queue NIC
  - A NIC has multiple queues
    - Each queue is mapped to a VM
  - L2 classifier in HW
    - Reducing receive-side overheads
  - Drawback
    - L2 SW switch is still need
  - e.g., Intel VT-c VMDq
Enhance KVM for Intel® Virtualization
Technology for Connectivity [KVMForum’08]

---
HW Support: CDNA
HW Support: CDNA
CDNA: Concurrent Direct Network Access
  - Rice Univ.’s project
  - Research prototype: FPGA-based NIC
    - SW-based DMA protection without IOMMU
Concurrent Direct Network Access in Virtual Machine Monitors [HPCA’07]

---
HW Support: SR-IOV
HW Support: SR-IOV
SR-IOV (Single Rooted I/O Virtualization)
  - PCI-SIG standard
  - HW NIC virtualization
    - Virtual function is accessed as
   an independent NIC by a VM
    - No VMM intervention in I/O path
Intel 82599 10Gb NIC
Enhance KVM for Intel® Virtualization
Technology for Connectivity [KVMForum’08]
Source: http://www.maximumpc.com/article/maximum_it/intel_launches_industrys_first_10gbaset_server_adapter

---
Network Optimization Research
Network Optimization Research
Architectural optimization
  - Diagnosing Performance Overheads in the Xen Virtual Machine Environment [VEE’05]
  - Optimizing Network Virtualization in Xen [USENIX’06]
- I/O virtualization optimization
  - Bridging the Gap between Software and Hardware Techniques for I/O Virtualization [USENIX’08]
  - Achieving 10 Gb/s using Safe and Transparent Network Interface Virtualization [VEE’09]

---
Inter-VM Communication
Inter-VM Communication
Analogous to inter-process communication (IPC)
  - Split driver model has unnecessary path for inter-VM communication
    - Dom1  Dom0 (bridge)  Dom2
Xen network architecture
Dom1
Dom2
vif1.0
Dom0
eth0
eth0
Bridge
vif2.0
eth0
VMM
H/W

---
Inter-VM Communication
Inter-VM Communication
High-performance inter-VM communication based on shared memory
Research projects
  - Depending on which layer is interposed for inter-VM communication
    - XenSocket [Middleware’07]
    - XWAY [VEE’08]
    - XenLoop [HPDC’08]
    - Fido [USENIX’09]

---
Inter-VM Communication: XWAY
Inter-VM Communication: XWAY
XWAY
  - Socket-level inter-VM communication
    - Inter-domain socket communications supporting high performance and full binary compatibility on Xen [VEE’08]
Interface based on
shared memory

---
Inter-VM Communication: XenLoop
Inter-VM Communication: XenLoop
XenLoop
  - Driver-level inter-VM communication
    - XenLoop: a transparent high performance inter-vm network loopback [HPDC’08]
Module-based
implementation
 Practical

---
Summary
Summary
I/O virtualization
  - Focused on reducing performance overheads
    - Network virtualization overhead matters in 10Gbps network
  - Prevalent paravirtualized I/O
    - Module-based split driver model has been adopted in mainline
  - HW support for I/O virtualization
    - SR-IOV NIC & IOMMU mostly eliminates I/O virtualization overheads

---
GPU Virtualization
GPU Virtualization

---
GPU is I/O device or Computing unit?
GPU is I/O device or Computing unit?
Traditional graphics devices
  - GPU as an I/O device (output device)
    - Framebuffer abstraction
      - Exposing screen area as a memory region
    - 2D/3D graphics acceleration
      - Offloading complex rendering operations from CPU to GPU
        - Library: OpenGL, Direct3D
      - Why offloading?
        - Graphics operations are massively parallel in a SIMD manner
        - GPU is a massively parallel device with hundreds of cores
- Why not a computing device?
  - General-purpose GPU (GPGPU)
    - Not only handling graphics operations, but also processing general parallel programs
    - Library: OpenCL, CUDA

---
GPU Virtualization
GPU Virtualization
SW-level approach
  - GPU multiplexing
    - A GPU is shared by multiple VMs
    - Two approaches
      - Low-level abstraction: Virtual GPU (device emulation)
      - High-level abstraction: API remoting
- HW-level approach
  - Direct assignment
    - GPU pass-through
    - Supported by high-end GPUs
GPU Virtualization on VMware’s Hosted I/O Architecture [OSR’09]

---
SW-Level GPU Virtualization
SW-Level GPU Virtualization
Virtual GPU vs. API Remoting
	Virtual GPU	API remoting
Method	Virtualzation at GPU device level	Virtualiztion at API level / (e.g., OpenGL, DirectX)
Pros	Library-independent	VMM-independent / GPU-independent
Cons	VMM-dependent / GPU-dependent /  Most GPUs are closed and rapidly evolving, so virtualization is difficult	Library-dependent / But, a few libraries (e.g., OpenGL, Direct3D) are prevalently used / (# of libraries < # of GPUs)
Use case	Base emulation-based virtualization (e.g., Cirrus, VESA)	Guest extensions used by most VMMs (Xen, KVM, VMware)

---
API Remoting: VMGL
API Remoting: VMGL
OpenGL apps in X11 systems
VMGL: VMM-Independent Graphics Acceleration [XenSummit’07, VEE07]

---
API Remoting: VMGL
API Remoting: VMGL
VMGL apps in an X11 guest VM
VMGL: VMM-Independent Graphics Acceleration [XenSummit’07, VEE07]

---
API Remoting: VMGL
API Remoting: VMGL
VMGL on KVM
  - API remoting is VMM-independent
  - WireGL protocol provides efficient 3D remote rendering
QEMU
Guest VM
Viewer
Quake3
VirtIO-Net
Backend
X Server
VMGL
Library
VMGL stub
Guest OS
VirtIO-Net
Frontend
KVM (kernel module)
Host OS
(Linux)

---
HW-Level GPU Virtualization
HW-Level GPU Virtualization
GPU pass-through
  - Direct assignment of GPU to a VM
  - Supported by high-end GPUs
  - Two types (defined by VMware)
    - Fixed pass-through 1:1
      - High-performance, but low scalability
    - Mediated pass-through 1:N
GPU provides multiple context,
so a set of contexts can be directly assigned to
each VM
GPU Virtualization on VMware’s Hosted I/O Architecture [OSR’09]

---
Remote Desktop Access: Industry
Remote Desktop Access: Industry
Remote desktop access technologies for high UX
  - Citrix HDX
  - Microsoft RemoteFX
  - Teradici PCoIP (PC-over-IP)
- VDI solutions
  - VMware View with PCoIP
    - VMware ESXi + PCoIP
  - Citrix XenDesktop
    - Xen + HDX + RemoteFX
  - Microsoft VDI with RemoteFX
    - Hyper-V + RemoteFX
  - VirtualBridges VERDE VDI
    - KVM + SPICE

---
Remote Desktop Access: Open Source
Remote Desktop Access: Open Source
SPICE
  - Remote interaction protocol for VDI
    - Optimized for virtual desktop experiences
    - Actively developed by Redhat
    - Based on KVM

---
Remote Desktop Access: Open Source
Remote Desktop Access: Open Source
SPICE (cont’)
Separate display thread per VM
(display rendering parallelization)
A VM (KVM) =
    I/O thread (QEMU main)
    + Display thread
    + VCPU0 thread
    + VCPU1 thread
    …

---
Summary
Summary
GPU virtualization
  - GPU is mostly closed
    - Low-level GPU virtualization is technically complicated
    - Instead, high-level abstraction well hides underlying complexity
      - API remoting is an appropriate solution
  - GPU is not only for client devices, but also for servers
    - Virtual desktop infrastructure (VDI)
    - GPU instance provided by public clouds
      - Cluster GPU Instances for Amazon EC2